## Slide 1: Joshua and Joseph's IoT Final Project
Protecting the space around vulnerable areas with an IoT alarm and counter-measure system.

## Slide 2: A Description of Our Problem: General security and alarm system to protect vulnerabilities/valuables *Needs to include: Detection, Response, Connectivity, and Modes
To protect an area in case of intrusion and malicious intent.
A low-cost solution to detect presence and respond quickly.
Includes mode control

## Slide 3: How our IoT solution works: Sensing/Actuating, MQTT comms, MongoDB, Dashboard, React App
Sensors send data to ESP32
--> ESP32 sends data to MQTT Broker
--> MQTT Broker publishes data via Data Topic
--> React App, Dashboard, and MongoDB are subscribed to Data Topic
--> App and Dashboard show users updated data in real time
--> Commands can be sent from Dashboard or App via Command Topic
--> ESP32 is subscribed to the Command Topic
--> ESP32 sets system mode according to command received

## Slide 4: The hardware we use: Sensors and Actuators
ESP32: main control unit for hardware
PIR Motion Sensor: HC SR-501 infrared motion sensor
Sonar Sensor: HC-SR04 ultrasonic ranging module
LED and 220Ohm resistor
4 piezo buzzers

## Slide 5: What software we used:
ESP32 Firmware:
-Reads PIR and sonar data
-Determines presence
-Activates LED and buzzers based on current mode
-Published status/data and is subscribed to receive commands
-Code is uploaded via Arduino IDE
MQTT Messages:
-Data topic messages have a format similar to:
{"mode":"AUTO",
"presence":"true,
"actuators":true}
-Command topic messages are similar to:
{"COMMAND":"ON",
"TIMESTAMP":"…",
"SOURCE":"REACT_APP"}
User Interfaces:
-React Snack app publishes commands and shows latest system status
-Dashboard/database provide additional monitoring
-Our project supports 3 modes:
AUTO: actuators are active only when a presence is detected
ON: actuators are active constantly, regardless of presence detection
OFF: actuators do not activate ever

## Slide 6: Security Implementation:
-Potential Risks Addressed:
Malformed MQTT messages
Unexpected fields or data types
Oversized payloads
Unknown commands
-Checks implemented:
Require JSON structure
Verify required field names
Check field count, types, and sizes
Allow only approved command values

## Slide 7: A quick Demo! Here's what we'll be showing:
Our ESP32, sensors, and actuators
Live data uploaded to the database and shown on our Dashboard and React App.
Live triggering of our actuators when presence is detected.
What different modes do for our system.
Any volunteers?